## Slide 1: Concolic Testing for High Test Coverage and Reduced Human Effort in Automotive Industry
Yunho Kim, SWTV group
KAIST, South Korea
Dongju Lee
Junki Baek
Moonzoo Kim

## Slide 2: Manual Testing in Automotive Industry: - Large Human Effort Required
Manual Testing
Achieving high reliability requires large human effort
SW reliability is critical for cars
1MLoC / a car * 10 models 7KLoC/MM
…
Toyota “Unintended Acceleration” has killed 89
Tesla fatal crash was on Autopilot
= 120MYr (for coverage testing)
Notes: Achieving high coverage requires large human effort because Automotive SW is large and complex due to many sources of inputs and complex logic.
Automotive SW 이미지 (자동차를 사람이 밀고 (시동꺼진 차))
예. 분기 커버리지 달성에 100 LOC = 1.5 MM
ISO 26262
테슬라 차 사고 => SW 신뢰성이 매우 억수로 중요. => 매우 복잡한 MC/DC 테스팅 인력 억수로 많이 들고 힘듦

## Slide 3: Automated Testing can Achieve High Reliability and Reduce Human Testing Effort
Automated Testing
Automated testing can be 100x faster than manual one
1MLoC/a car * 10 models
= 1.2CYr (= 0.1M on 100 cloud cores)
700KLoC/1CM
…
Automated testing achieves high reliability
Detecting
hidden bugs
Achieving high code coverage
Notes: 2페이지랑 동일한 레이아웃, 박스로 구분
Automated testing is 100x faster than manual testing and reduce manual testing effort.
100 cores, 1.2 yr
예. 분기 커버리지 달성에 100 LOC = 1.5 MM
ISO 26262
테슬라 차 사고 => SW 신뢰성이 매우 억수로 중요. => 매우 복잡한 MC/DC 테스팅 인력 억수로 많이 들고 힘듦

## Slide 4: Benefits of Unit Testing
Bug correction time: 3x faster than system testing
  3.25 hours vs 11.5 hours
Source: B. Boehm and V. Basil, Software Defect Reduction Top 10 List, IEEE Computer, January 2001
Source: Capers Jones, Applied Software Measurement: Global Analysis of Productivity and Quality
Bug correction cost: 7x cheaper than system tests
  $937 (unit test) vs $7,136 (system test)
Excerpted from the CONBRIO paper slides [Kim et al., ICSE18]
Notes: All of us know that unit testing has benefits over system testing. Unit testing is 7 times cheaper than system testing to detect and fix a bug as well as unit testing is 3 times faster than system testing to run and detect a bug. Unfortunately, such benefits of unit testing is not much enjoyed in real-world because of false alarm problems. To run a target unit in an isolated environment for unit testing, we have to write down stub and mock functions to provide contexts to the unit. If such stub and mock functions provide inaccurate context, unit testing raises a false alarm, which is feasible in unit execution, but infeasible in system execution. Such false alarm problem is severe in automated unit test generation techniques because such techniques do not know the appropriate context of the target unit. To address such false alarm problems in automated unit test generation techniques, we propose two ideas

## Slide 5: Importance of Automated Unit Testing In Automotive SW
System testing is expensive and less effective
  Full vehicle HW and human drivers are required
  Driving a car with various physical environments spends a lot of time
  Hard-to-achieve high test coverage due to low controllability
Unit testing is cheap and more effective
  Full vehicle HW and human drivers are NOT necessary
  No need to drive a car
  Easy-to-achieve high coverage due to high controllability
VS
Notes: Unit testing 서서히 나타나는 애니메이션으로
Compared to system testing requires lots of resources,
Unit testing rmfla\
비주얼
자동차 테스트 장비 등

## Slide 6: 3 Technical Challenges for Automated Unit Testing
False alarms
struct S : 4 Bytes
5bits
18bits
char x
int y:5
int z:18
Bit-fields
Function pointers
Notes: To achieve high test coverage using automated testing, we need to address 3 technical challenges to address
False alarm 그림 다시

## Slide 7: False Alarms due to Infeasible Unit Executions
False alarms can be raised due to missing contexts
Erroneous behaviors
(e.g., NULL-ptr deref, )
Target unit’s REAL behavior w/
proper contexts in a pgm P
False alarm
Erroneous behaviors
(e.g., NULL-ptr deref, )
Target unit’s behavior
w/o any contexts
Notes: False alarms
False alarm 나타낼 더 명확한 그림(bug가 아니어야 함)

## Slide 8: No Support of Symbolic Bit-fields
Tracking symbolic expression for bit-fields is NOT possible
  bit-fields are NOT addressable (i.e., &(s.y) is not allowed)
1: struct S{
2: char x;
3: int y:5;
4: int z:18;};
Memory address (key) | Sym. Exp. (value)
&(S.x) | S.x0+3
&(S.y) NOT allowed | N/A
&(S.z) NOT allowed | N/A
Symbolic Memory Map
Notes: 18 bits, 5 bits (띄어쓰기)
Bitfield 왜 사용하나 설명
그림으로 (pictorial) 하게

## Slide 9: No Support of Symbolic Function Pointers
Hard-to-know which function a given func. ptr. points to
*fnPtr(x,y)
add(x,y)
sub(x,y)
mul(x,y)
Notes: Add, sub, mul clipart 추가
그림으로 (pictorial) 하게

## Slide 10: Overview of MAIST
MAIST
Test input
generator
MAIST
Converter
MAIST
Test harness generator
Coverage
Report
Test cases
Test
drivers/
stubs
Target
C code p
Target
C code p’
CROWN
C code
MAIST
External tool
Legend
Driver gen.
Stub gen.
Bit-field transform.
Search strategy coordinator
CROWN features
- Bit-level accuracy
- Easy-to-extend
- Low memory overhead
- Fast through lightweight instr.
Sol. 1: Task-oriented
driver/stub gen. to
reduce false alarms
Sol. 2: Bit-field
transform. to support
sym. bit-fields
Sol. 3: Static
analysis to support
sym. function pointer
Notes: 말풍선 사라지지 않게
CROWN features
솔루션이랑 매칭되게

## Slide 11: Unit Testing f without Contexts of f
Without Contexts of f
Pros: fast exploration of target unit execution paths
Cons: infeasible target unit executions
With Contexts of f
Pros: reduced infeasible target
unit executions
Cons: slow exploration of target unit execution due to large cost of
exploring context functions
Excerpted from the CONBRIO paper slides [Kim et al., ICSE18]
Unit Testing f with Contexts of f
Notes: If we perform unit testing on a target function f without its contexts functions such as f’s callers and f’s callees,
+ the unit testing can be very fast because f’s code size is small.
But, we are testing f without any constraints enforced by f’s real contexts, many infeasible target unit executions may occur which can raise false alarms.
In contrast, if we utilize the context functions of a target function f,
+ we can reduce infeasible target unit executions because the context functions enforces realistic constraints to target unit executions
- But, unit testing becomes slow and misses bugs because target unit execution paths may not be fully explored in given time budget of unit testing. This is because we have to also explore the execution paths of the context functions (shown as light blue arrows).
Therefore, we have clear trade-off between unit testing accuracy and unit testing cost by the decision of how much target unit context to include in unit testing.
We propose the 2 ideas to identify and utilize sweet spot of this trade-off so that unit testing can be *both effective and accurate* using

## Slide 12: Task-oriented Unit-test Driver/Stubs Generation
f
s1
s2
s3
h
g
stub_h
s5
driver_f
s4
driver_g
file1.c
file2.c
sym_harness.c
Task t1
Task t2
  A Task is a mostly minimal independent unit
File scope
Entry function
Static function
Function call
Legend
Driver/stub functions
Notes: 자동차 DOMAIN 의 특성상 task 위주의 개발을 하게 되는데
이유1.
이유2.
…..
Task oriented unit testing is a key to the success of MAIST

## Slide 13: Bit-field Transformation
Original program p | Transformed program p’
n=S.z+1; | n=(((S_nb.ba0[2]&127)<<16)¦ (S_nb.ba0[1]<<8)¦ S_nb.ba0[0])>>5 +1;
S.z=S.x+3; | S_nb . ba0 [2]= ((((S_nb.x+3) <<5) > >(2*8)) &127)¦ (S_nb .ba0 [2]&128); S_nb . ba0 [1]= (((S_nb.x+3) <<5) > >(1*8)) &255; S_nb . ba0 [0]= (((S_nb.x+3) <<5) &224) ¦ ( S_nb .ba0 [0]&31);
high address
low address
struct S : 4 Bytes
1: struct S{
2: char x;
3: int y:5;
4: int z:18;};
1: struct S_nb{
2: char x;
3: unsigned char ba0[3];
4: } ;
struct S_nb : 4 bytes
ba0[2] | ba0[1] | ba0[0] | x
5 bits
18 bits
char x
int y:5
int z:18
Notes: 회색 진하게

## Slide 14: Symbolic Function Pointer Support
target.c
1:int (*fnPtr)(int,int);
2:int add(int,int) {…}
3:int sub(int,int) {…}
3:int mul(int,int) {…}
4:void f() {…
5: fnPtr=add;}
6:int g(){…
7: fnPtr=sub;}
7:int h(){…
8: fnPtr=mul;}
8:void do_chk(int model){
9:…
10: int ret=fnPtr(x,y);
11: …}
Function pointer input
Candidate1: add()
Candidate2: sub()
harness_target.c
1:void drv_do_chk(){
2: …
3: SYM_int(sym_choice);
4: switch(sym_choice){
5: case 0:
6: fnPtr=add;
7: break;
8: case 1:
9: fnPtr=sub;
10: break;
11: case 2:
12: fnPtr=mul;
13: default: break;}
14: SYM_int(p1);
15: do_chk(p1);}
Step 2: Set *fnPtr as one of the candidates using a symbolic var sym_choice
Set *fnPtr as add()
if sym_choice==0
Set *fnPtr as sub()
if sym_choice==1
Candidate3: mul()
Set *fnPtr as mul()
if sym_choice==2
Step 1: Identifying candidate functions using static analysis
Notes: 함수 포인터 +, -, *로 3개
12-13 한 장으로

## Slide 15: Research Questions
RQ1-2: Overall benefit of MAIST
RQ1: How much
test coverage
does MAIST achieve?
RQ2: How much
human test effort
does MAIST reduce?
Notes: RQ4-6 은 달라보이게 시각적으로

## Slide 16: Research Questions
RQ3: Effect of Task-oriented test Gen.
RQ4: Effect of Sym. bit-fields
RQ5: Effect of Sym. Func. Ptr.
RQ3-5: Effectiveness of MAIST for addressing the technical difficulties
False alarm
Notes: RQ4-6 은 달라보이게 시각적으로

## Slide 17: Overview of Target SW: Integrated Body Unit
Smart Key (SMK)
  Remote door lock/unlock
  Button start
Module | #files | #tasks | #functions | LoC | Avg. CC per func.
BCM | 27 | 143 | 656 | 53,690 | 4.3
SMK | 198 | 554 | 2,521 | 135,877 | 5.8
TPMS | 29 | 68 | 302 | 16,951 | 4.1
Total | 254 | 767 | 3,479 | 206,518 | 4.9
Body Control Module (BCM)
  Wiper, door control
  Burglar alarm
Tire Pressure Monitor (TPM)
  Tire pressure sensing
IBU
Notes: LoC

## Slide 18: RQ1:MAIST Achieved 90.5% Branch and 77.8% MC/DC Cov.
* Running 20 hours on 12 CPU cores (3.0GHz)
Chart: %funcs in branch cov. range
| [20%,40%) | [40%,60%) | [60%,80%) | [80%,100%) | 100%
 | 0.031 | 0.057 | 0.093 | 0.097 | 0.722
Chart: %funcs in MC/DC cov. range
| [20%,40%) | [40%,60%) | [60%,80%) | [80%,100%) | 100%
 | 0.043 | 0.09 | 0.131 | 0.164 | 0.5712
  100% branch cov. of 72.2% of funcs
  100% MC/DC cov. of 57.1% of funcs
Notes: 그래프 label
메시지 각 RQ별로 (BR > 90, 90.5%) almost all possible
빠진 uncovered branches RQ 다시 넣기

## Slide 19: RQ2. MAIST Reduced Testing Cost from 30MM to 5MM (↓83.3%)
Chart: 
| Manual testing
MM | 30
IBU code
210KLoC
7KLoC/MM
(cov. testing)
Manual testing cost
MAIST
Development
(one time cost!)
Manual testing for 9.5% uncovered brs
30MM
5MM
9MM
Notes: 5mm 9mm 공간 띄어서
9mm 색 변경 (회색, 연노랑)
30MM(붉은색)이랑 5MM 색 다르게
Cost of manual testing of IBU
  210KLoC (IBU LoC) / (350 LoC (LoC that 1 engineer can handle in a day) * 20 business day) = 30 MM
Cost of automated testing of MAIST
  9 MM (to develop MAIST and train engineers to use MAIST) + 5 MM (to cover 9.5% of branches that MAIST did not cover)

## Slide 20: RQ2: Analysis of the Uncovered Branches
Reasons | #uncovered brs | Ratio (%)
Imprecise stub | 43 | 41.7
Path explosion | 21 | 20.4
Static local variable | 21 | 20.4
Imprecise driver | 10 | 9.7
Unreachable branches | 8 | 7.8
Total | 103 | 100
Imprecise stub is the main cause of uncovered branches
  Manually analyze 33 BCM functions having <60% br. Cov.
Notes: 메시지 각 RQ별로 (BR > 90, 90.5%) almost all possible
빠진 uncovered bran
We manually analyzed the uncovered branches of BCM as
an example. Among the 66 (=0+14+52) functions in BCM
whose branch coverage is less than 60%, we selected the
largest 33 functions in terms of the number of branches.ches RQ 다시 넣기

## Slide 21: RQ3:No false crash alarms by Task-oriented driver/stub generation
Chart: 
| Function-oriented | Task-oriented
#false alarms | 146 | 0
No false crash alarm at all!
146
#false crash alarms
Function-oriented
unit testing
Task-oriented Unit testing (MAIST)
Notes: 그래프 label
그래프에서 그라데이션 전부 삭제

## Slide 22: RQ4: Symbolic Bit-fields Support Highly Increases Test Coverage
Notes: 그래프 label
그래프로 작성 예정

## Slide 23: RQ5: Sym. Function Pointer Support Increases Test Coverage
Notes: 그래프로 작성 예정

## Slide 24: Conclusion

## Slide 25: Concolic Testing for High Test Coverage and Reduced Human Effort in Automotive Industry
Yunho Kim, SWTV group
KAIST, South Korea
Dongju Lee
Junki Baek
Moonzoo Kim