## Slide 1: Key Difference between Manual Testing and Model Checking
Manual testing (unit testing)
  A user should test one concrete execution scenario by checking a pair of concrete input values and the expected concrete output values
Model checking (concolic testing)
  A user should imagine all possible execution scenarios and model a general environment that can enable all possible executions
  A user should describe general invariants on input values and output values

## Slide 2: Ex1. Circular Queue of Positive Integers
0 | 0 | 0 | 0 | 0 | 0 | 15 | 6 | 9 | 8 | 4 | 0
3 | 5 | 0 | 0 | 0 | 0 | 15 | 6 | 9 | 8 | 4 | 17
3 | 5 | 0 | 0 | 0 | 0 | 0 | 6 | 9 | 8 | 4 | 17
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
head=6
tail=11
tail=2
head=6
tail=2
head=7
Step 1)
#include<stdio.h>
#define SIZE 12
#define EMPTY 0
// We assume that q[] is // empty if head==tail
unsigned int q[SIZE],head,tail;
void enqueue(unsigned int x) {
q[tail]=x;
tail=(++tail)%SIZE;
}
unsigned int dequeue() {
unsigned int ret;
ret = q[head];
q[head]=0;
head= (++head)%SIZE;
return ret;}
Step 2)
Step 3)

## Slide 3
void enqueue_verify() {
unsigned int x, old_head, old_tail;
unsigned int old_q[SIZE], i;
__CPROVER_assume(x>0);
for(i=0; i < SIZE; i++) old_q[i]=q[i];
old_head=head;
old_tail=tail;
enqueue(x);
assert(q[old_tail]==x);
assert(tail== ((old_tail +1) % SIZE));
assert(head==old_head);
for(i=0; i < old_tail; i++) assert(old_q[i]==q[i]);
for(i=old_tail+1; i < SIZE; i++) assert(old_q[i]==q[i]);
}
void dequeue_verify() {
unsigned int ret, old_head, old_tail;
unsigned int old_q[SIZE], i;
for(i=0; i < SIZE; i++) old_q[i]=q[i];
old_head=head;
old_tail=tail;
__CPROVER_assume(head!=tail);
ret=dequeue();
assert(ret==old_q[old_head]);
assert(q[old_head]== EMPTY);
assert(head==(old_head+1)%SIZE);
assert(tail==old_tail);
for(i=0; i < old_head; i++) assert(old_q[i]==q[i]);
for(i=old_head+1; i < SIZE; i++) assert(old_q[i]==q[i]);}
int main() {// cbmc q.c –unwind SIZE+2
environment_setup();
enqueue_verify();}
int main() {// cbmc q.c –unwind SIZE+2
environment_setup();
dequeue_verify();}

## Slide 4
#include<stdio.h>
#define SIZE 12
#define EMPTY 0
unsigned int q[SIZE],head,tail;
void enqueue(unsigned int x) {
q[tail]=x;
tail=(++tail)%SIZE;
}
unsigned int dequeue() {
unsigned int ret;
ret = q[head];
q[head]=0;
head= (++head)%SIZE;
return ret;
}
// Initial random queue setting following the script
void environment_setup() {
int i;
for(i=0;i<SIZE;i++) { q[i]=EMPTY;}
head=non_det();
__CPROVER_assume(0<= head && head < SIZE);
tail=non_det();
__CPROVER_assume(0<= tail && tail < SIZE);
if( head < tail)
for(i=head; i < tail; i++) {
q[i]=non_det();
__CPROVER_assume(0< q[i]);
}
else if(head > tail) {
for(i=0; i < tail; i++) {
q[i]=non_det();
__CPROVER_assume(0< q[i]);
}
for(i=head; i < SIZE; i++) {
q[i]=non_det();
__CPROVER_assume(0< q[i]);
}
} // We assume that q[] is empty if head==tail
}

## Slide 5: Model checking v.s. random sequence of method calls
You may try to test the circular queue code by calling enqueue and dequeuer randomly
  Ex.
  void test1(){e(10);r=d();assert(r==10);) void test2(){e(10);e(20);d();e(30);r=d(); assert(r =20);) void test3(){...} …
Note that model checking covers all test scenarios of the above random method sequence calls
  Note that a random sequence of method calls just provide ONE input instance/state to the circular queue
  MC provides ALL input instances/states through environment/input space modeling

## Slide 6: Ex2. Tower of Hanio
  Write down a C program to solve the Tower of Hanoi game (3 poles and 4 disks) by using CBMC
  Hint: you may non-deterministically select the disk to move
  Find the shortest solution by analyzing counter examples. Also explain why your solution is the shortest one.
    Use non-determinism and __CPROVER_assume() properly for the moving choice
    Use assert statement to detect when all the disks are moved to the destination

## Slide 7: // cbmc hanoi3.c –unwind 7 –no-unwinding-assertions // Increase n from 1 to 10 in –unwind [n] to find the shortest solution 1:signed char disk[3][3] = {{3,2,1},{0,0,0},{0,0,0}}; 2:char top[3]={2,-1,-1};// The position where the top disk is located at. 3: // If the pole does not have any disk, top is -1 4:int main() { 5: unsigned char dest, src; 14: while(1) { 15: src = non_det(); 16: __CPROVER_assume(src==0 || src==1 || src==2); 17: __CPROVER_assume(top[src] != -1); 18: 19: dest= non_det(); 20: __CPROVER_assume((dest==0 || dest==1 || dest==2) && (dest != src)); 21: __CPROVER_assume(top[dest]==-1 || (disk[src][top[src]] < disk[dest][top[dest]]) ); 22: 25: top[dest]++; 26: disk[dest][top[dest]]=disk[src][top[src]]; 27: 28: disk[src][top[src]]=0; 29: top[src]--; 30: 31: assert( !(disk[2][0]==3 && disk[2][1]==2 && disk[2][2]==1 )); } }
1 | 0 | 0
2 | 0 | 0
3 | 0 | 0
0 1 2
2
1
0
2 | -1 | -1
Top[3]
0 | 0 | 1
0 | 0 | 2
0 | 0 | 3
0 1 2
2
1
0