## Slide 1: Coherence
Jaehyuk Huh
Computer Science, KAIST
Part of slides are based on CS:App from CMU

## Slide 2: Two Classes of Protocols
Sharing state : which caches have a copy for a given address?
Snoop-based protocols
  No centralized repository for sharing states
  All requests must be broadcast to all nodes : don’t know who may have a copy…
  Common in small-/medium sized shared memory MPs
  Has been hard to scale due to the difficulty of efficient broadcasting
  Most commercial MPs up to ~64 processors
Directory-based protocols
  Logically centralized repository of sharing states : directory
  Need a directory entry for every memory blocks
  Invalidation requests go to the directory first, and forwarded only to the sharers
  A lot of research efforts, but only a few commercial MPs

## Slide 3: Snoop-based Cache Coherence
No explicit sharing state information  all caches must participate in snooping
Any cache miss request must be put on the bus
All caches and memory observe bus requests
All caches snoop a request and check it cache tags
Caches put responses
  Just sharing state (I have a copy !)
  Data transfer (I have a modified copy, and am sending it to you!)
Memory
$
$
$
$
P1
P2
P2
P2

## Slide 4: Architecture for Snoopy Protocols
Extended cache states in tags
  Cache tags must keep the coherence state (extend Valid and Dirty bits in single processor cache states)
Broadcast medium (e.g. bus)
  Need to send all requests (including invalidation) to other caches
  Logically a set of wires connect all nodes and memory
Serialization by bus
  Only one processor is allowed to send invalidation
  Provide total ordering of memory requests
Snooping bus transactions
  Every cache must observe all the transactions the bus
  For every transaction, caches need to lookup tags to check any actions is necessary
  If necessary, snoop may cause state transition and new bus transaction

## Slide 5: Cache State Transition
Cache controller
  Determines the next state
  State transition may initiate actions, sending bus transactions
Two sources of state transition
  CPU: load or store instructions
  Snoop: request from other processors
Snoop tag lookup
  Need to snoop all requests on the bus
  Consume a lot of cache tag bandwidth
  May add duplicate tags only for snoop
  Two identical tags, one for CPU requests and the other for snoop
  Duplicate tags must be synchronized

## Slide 6: MSI Protocol
Simple three state protocols
M (Modified)
  Valid and dirty
  Only one M state copy can exist for each block address in the entire system
  Can update without invalidating other caches
  Must be written back to memory when evicted
S (Shared)
  Valid and clean
  Other caches may have copies
  Cannot update
I (Invalid)
  Invalid
State transition diagrams in the next four slides, D. Pattern, EECS, Berkeley

## Slide 7: State Transition
CPU requests
  Processor Read (PrRd): load instruction
  Processor Write (PrWr): store instruction
  Generate bus requests
Bus requests (snoop)
  Bus Read (BusRd)
  Bus RFO (BusRFO): Read For Ownership
  Bus Upgrade (BusUp)
  Bus Writeback (BusWB)
  May need to send data to the requestor
Notation: A / B
  A : event which causes state transition
  B : action generated by state transition

## Slide 8: MSI State Transition - CPU
State transition by CPU requests
PrRd / ---
Invalid
Shared
(read/only)
Modified
(read/write)
PrRd / BusRd
PrWr / BusRFO
PrWr / BusUp
PrRd / ---
PrWr / ---

## Slide 9: MSI State Transition - Snoop
State transition by bus requests
Invalid
Shared
(read/only)
Modified
(read/write)
BusRFO / BusWB
BusUp / BusWB
BusRd / BusWB
BusRd / ---
BusRFO / ---
BusUp / ---

## Slide 10: Example
Step | P1 |  | P2 |  | P3 |  | Bus |  | Mem
 | State | Value | State | Value | State | Value | Action | Proc | Value
 | I |  | I |  | I |  |  |  | 10
P1 read A | S | 10 | I |  | I |  | BusRd | P1 | 10
P2 read A | S | 10 | S | 10 | I |  | BusRd | P2 | 10
P2 write A (20) | I |  | M | 20 | I |  | BusUp | P2 | 10
P3 read A | I |  | S | 20 | S | 20 | BusRd | P3 | 20
P1 write A (30) | M | 30 | I |  | I |  | BusRFO | P1 | 20

## Slide 11: Supporting Cache Coherence
Coherence
  Deal with how one memory location is seen by multiple processors
  Ordering among multiple memory locations  Consistency
  Must support write propagation and write serialization
Write Propagation
  Write become visible to other processors
Write Serialization
  All writes to a location must be seen in the same order by all processes
  For two writes w1 and w2 for a location A
  If a processor sees w1 before w2,
   all processor must see w1 before w2

## Slide 12: Review Snoop-based Coherence
No explicit sharing state
  Requestor cannot know which nodes have copies
  Broadcast request to all nodes
  Every node must snoop all bus transactions
Traditional implementation uses bus
  Allow one transaction at a time  will be relaxed later
  Serialize all memory requests (total ordering)  will be relaxed later
Write serialization
  Conflicting stores are serialized by bus

## Slide 13: Review From MSI Protocols
Load  store sequence is common
    Load R1, 0 (R10)  bring in read only copy
    Add R1, R1, R2
    Store R1, 0 (R1)  need to upgrade for modification
High chance that no other caches have a copy
  Private data are common (especially in well-parallelized programs)
  Even shared data may not be in others’ caches (due to limited cache capacity)
MSI protocols
  Always installs a new line in S state
  Subsequent store will cause write miss to upgrade the state to M

## Slide 14: MESI Protocols
Add E (Exclusive) state to MSI
E (Exclusive)
  Valid and clean
  No other caches have a copy of the block
Must check sharing state when install a block
  For BusRd transaction, all nodes will place a response: either snoop hit (“I have a copy”) or snoop miss (“I don’t have a copy”)
  If no other cache has a copy, new block is installed in E state
  If any cache has a copy, new block is installed in S state
E  M transition is free (no bus transaction)
  Exclusivity is guaranteed in E state
  For stores, upgrade E to M state without sending invalidations

## Slide 15: MESI State Transition - CPU
PrRd / ---
Invalid
Shared
(read/only)
Modified
(read/write)
PrRd / BusRd
(snoop hit)
PrWr / BusRFO
Exclusive
(read/only)
PrWr / BusUp
PrWr / ---
PrRd / BusRd
(snoop miss)
PrRd / ---
PrWr / ---
PrRd / ---

## Slide 16: MESI State Transition - Snoop
Invalid
Shared
(read/only)
Exclusive
(read/only)
BusRFO / BusWB
BusUp / BusWB
BusRd / ---
BusRFO / ---
BusUp / ---
BusRd / ---
Modified
(read/write)
BusRd / BusWB
BusRFO / ---
BusUp / ---

## Slide 17: Example
Step | P1 |  | P2 |  | P3 |  | Bus |  | Mem
 | State | Value | State | Value | State | Value | Action | Proc | Value
 | I |  | I |  | I |  |  |  | 10
P1 read A | E | 10 | I |  | I |  | BusRd | P1 | 10
P1 write A (15) | M | 15 | I |  | I |  | None |  | 10
P2 read A | S | 15 | S | 15 | I |  | BusRd | P2 | 15
P2 write A (20) | I |  | M | 20 | I |  | BusUp | P2 | 15
P3 read A | I |  | S | 20 | S | 20 | BusRd | P3 | 20
P1 write A (30) | M | 30 | I |  | I |  | BusRFO | P1 | 

## Slide 18: Coherence Miss
3 traditional classes of misses
  cold, capacity, and conflict misses
New type of misses only in invalidation-based MPs
  Cache miss caused by invalidation
  P1 read address A (S state)
  P2 write to address A (I state in P1, M state in P2)
  P1 read address A  a cache miss caused by invalidation
Why coherence miss occurs? true and false sharing
True sharing
  Producer generate a new value (invalid a copy in consumer’s cache)
  Consumer read the new value
False sharing
  Blocks can be invalidated even if the updated part is not used

## Slide 19: True Sharing
Invalid
Y
Modified
T3
X
Shared
X
Shared
T1
Write Y
X
Invalidation
Shared
Y
Modified
T4
Y
Invalid
Y
Modified
T2
X
Reader
Writer
Write Y
Data
State
Read

## Slide 20: False Sharing
Reader
Writer
Shared
X
Shared
Invalid
A
Y
Modified
X
Invalid
A
Modified
T1
T2
T3
A
X
A
Y
A
X
Invalidation
Write Y
Data
State
Write Y
A
Read
A
Shared
Y
Modified
T4
Y

## Slide 21: Basic Operation of Directory
• k processors.
• With each cache-block in memory: k presence-bits, 1 dirty-bit
• With each cache-block in cache: 1 valid bit, and 1 dirty (owner) bit
• Read from main memory by processor i:
  • If dirty-bit OFF then { read from main memory; turn p[i] ON; }
  • if dirty-bit ON then { recall line from dirty proc (cache state to shared); update memory; turn dirty-bit OFF; turn p[i] ON; supply recalled data to i;}
• Write to main memory by processor i:
  • If dirty-bit OFF then { supply data to i; send invalidations to all caches that have the block; turn dirty-bit ON; turn p[i] ON; ... }
  • ...

## Slide 22: Example Directory Protocol (1st Read)
M
S
I
P1
$
E
S
I
P2
$
M
S
U
M
Dir
ctrl
ld vA -> rd pA
Read pA
R/reply
R/req
P1: pA
S
S

## Slide 23: Example Directory Protocol (Read Share)
M
S
I
P1
$
M
S
I
P2
$
M
S
U
M
Dir
ctrl
ld vA -> rd pA
R/reply
R/req
P1: pA
ld vA -> rd pA
P2: pA
R/req
R/_
R/_
R/_
S
S
S

## Slide 24: Example Directory Protocol (Wr to shared)
M
S
I
P1
$
M
S
I
P2
$
M
S
U
M
Dir
ctrl
st vA -> wr pA
R/reply
R/req
P1: pA
P2: pA
R/req
W/req E
R/_
R/_
R/_
Invalidate pA
Read for ownership pA
Inv ACK
RX/invalidate&reply
S
S
S
M
M
reply xD(pA)
W/req E
W/_
Inv/_
EX

## Slide 25: Example Directory Protocol (Wr to M)
M
S
I
P1
$
M
S
I
P2
$
D
S
U
M
Dir
ctrl
R/reply
R/req
P1: pA
st vA -> wr pA
R/req
W/req E
R/_
R/_
R/_
Reply xD(pA)
Write_back pA
Read for ownership pA
RX/invalidate&reply
M
M
Inv pA
W/req E
W/_
Inv/_
Inv/_
W/req E
W/_
I
M
W/req E
RU/_

## Slide 26: Multi-level Caches
Cache coherence : must use physical address  caches must be physically tagged
Two-level caches without inclusion property
  Both L1 and L2 must snoop
Two-level caches with complete inclusion property
  Snoop only L2 caches first
  If snoop hits L2, forward snoop request to L1
L1 may have modified copy
  Data must be flushed down to L2 and sent to other caches

## Slide 27: Snoopy-bus with Switched Networks
Physical bus (shared wires) does not scale well
Tree-based address networks (fat tree)
Ring-based address networks
Arbitration (serialization) point
How to serialize ?

## Slide 28: AMD HyperTransport
Snoop-based cache coherence
Integrated on-chip coherence and interconnection controllers (glue logics for chip connection)
Use point-to-point packet-based switched networks

## Slide 29: AMD HyperTransport
How to broadcast requests?
  Requests are sent to home node
  Home node broadcast requests to all nodes
Home node
  Node where the physical address are mapped to DRAM
  Statically determined by physical address
  Home node serialize accesses to the same address
Snoopy-based, but used point-to-point networks with home node as a serialization point
  Resemble directory-based protocols
Support various interconnection topologies

## Slide 30: Read Transaction

## Slide 31: Performance Scalability

## Slide 33: Intel QPI
Limitation of AMD HyperTansport
  All snoop requests are broadcast through Home node to avoid conflicts
  Home node serializes conflicting requests
What happen if snoop requests are sent to caches directly?
  What if two caches attempt to send ReadInvalidation to the same address?
Intel QPI
  Allow direct snoop requests from a requester to all nodes
  However, an extra ordered request is sent to Home node too.
  Home node checks any possible conflicts and resolve the conflicts only when a conflict occurs

## Slide 34: Coherence within a Shared Cache
Multiple cores sharing an LLC (L3 cache usually)
How to make multiple L1s and L2s coherenct?