## Slide 1: Consistency
Jaehyuk Huh
Computer Science, KAIST
Part of slides are based on CS:App from CMU

## Slide 2: What is Consistency ?
When must a processor see the new value?
P1: A = 0; P2: B = 0;
..... .....
A = 1; B = 1;
L1: if (B == 0) ... L2: if (A == 0) ...
Impossible for both if statements L1 & L2 to be true?
  What if write invalidate is delayed & processor continues?
Memory consistency
  What are the rules for such cases?
  Create uniform view of all memory locations relative to each other

## Slide 3: Coherence vs. Consistency
  A = flag = 0
  Processor 0 Processor 1
  A = 1; while (!flag);
  flag = 1; print A;
Intuitive result: P1 prints A = 1
Cache coherence
  Provide consistent view of a memory location
  Does not say anything about the ordering of two different locations
Consistency can determine whether this code works or not

## Slide 4: Sequential Consistency
Lamport’s definition
“A multiprocessor is sequentially consistent if the result of any execution is the same as if the operations of all the processors were executed in some sequential order, and the operations of each individual processor occur in this sequence in the order specified by its program”
Most intuitive consistency model for programmers
  Processors see their own loads and stores in program order
  Processors see others’ loads and stores in program order
  All processors see same global load and store ordering

## Slide 5: Sequential Consistency
In-order instruction execution
Atomic loads and stores
SC is easy to understand but architects and compiler
writers want to violate it for performance
    Processor 1 Processor 2
    Store (a), 10; L: Load r1, (flag);
    Store (flag), 1; if r1 == 0 goto L;
    Load r2, (a);
initially flag = 0

## Slide 6: Memory Model Issues
Architectural optimizations that are correct for uniprocessors, often violate sequential consistency and result in a new memory model for multiprocessors
Slides from Prof. Arvind, MIT

## Slide 7: Committed Store Buffers
CPU
Cache
Main Memory
CPU
Cache
CPU can continue execution while earlier committed stores are still propagating through memory system
  Processor can commit other instructions (including loads and stores) while first store is committing to memory
  Committed store buffer can be combined with speculative store buffer in an out-of-order CPU
Local loads can bypass values from buffered stores to same address

## Slide 8: Example 1: Store Buffers
Suppose Loads can go ahead of Stores waiting in the store buffer: Yes !
Process 1 Process 2
Store (flag1),1; Store (flag2),1;
Load r1, (flag2); Load r2, (flag1);
Initially, all memory
locations contain zeros
Question: Is it possible that r1=0 and r2=0?
  Sequential consistency: No
Total Store Order (TSO):
IBM 370, Sparc’s TSO memory model
Slides from Prof. Arvind, MIT

## Slide 9: Example 2: Store-Load Bypassing
Process 1 Process 2
Store (flag1), 1; Store (flag2), 1;
Load r3, (flag1); Load r4, (flag2);
Load r1, (flag2); Load r2, (flag1);
Suppose Store-Load bypassing is permitted in the store buffer
  No effect in Sparc’s TSO model, still not SC
  In IBM 370, a load cannot return a written value until it is visible to other processors => implicity adds a memory fence, looks like SC
Question: Do extra Loads have any effect?
  Sequential consistency: No
Slides from Prof. Arvind, MIT

## Slide 10: Interleaved Memory System
CPU
Even Cache
Memory (Even Addresses)
Odd Cache
Memory (Odd Addresses)
Achieve greater throughput by spreading memory addresses across two or more parallel memory subsystems
  In snooping system, can have two or more snoops in progress at same time (e.g., Sun UE10K system has four interleaved snooping busses)
  Greater bandwidth from main memory system as two memory modules can be accessed in parallel

## Slide 11: Example 3: Non-FIFO Store buffers
With non-FIFO store buffers: Yes
Process 1 Process 2
Store (a), 1; Load r1, (flag); Store (flag), 1; Load r2, (a);
Sparc’s PSO memory model
Question: Is it possible that r1=1 but r2=0?
  Sequential consistency: No
Slides from Prof. Arvind, MIT

## Slide 12: Example 4: Non-Blocking Caches
Assuming stores are ordered: Yes because Loads can be reordered
Sparc’s RMO, PowerPC’s WO, Alpha
Question: Is it possible that r1=1 but r2=0?
  Sequential consistency: No
Process 1 Process 2
Store (a), 1; Load r1, (flag); Store (flag), 1; Load r2, (a);
Slides from Prof. Arvind, MIT

## Slide 13: Example 5: Speculative Execution
With speculative loads: Yes even if the stores are ordered
Process 1 Process 2
Store (a), 1; L: Load r1, (flag); Store (flag), 1; if r1 == 0 goto L;
Load r2, (a);
Question: Is it possible that r1=1 but r2=0?
  Sequential consistency: No
Slides from Prof. Arvind, MIT

## Slide 14: Address Speculation
Store (x), 1;
Load r, (y);
Instruction foo
All modern processor will execute foo speculatively by assuming x is not equal to y.
This also affects the memory model
Slides from Prof. Arvind, MIT

## Slide 15: Example 6: Store Atomicity
Even if Loads on a processor are ordered, the different ordering of stores can be observed if the Store operation is not atomic.
Process 1 Process 2 Process 3 Process 4
Store (a),1; Store (a),2; Load r1, (a); Load r3, (a);
Load r2, (a); Load r4, (a);
Question: Is it possible that r1=1 and r2=2 but r3=2 and r4=1 ?
  Sequential consistency: No
Slides from Prof. Arvind, MIT

## Slide 16: Example 8: Causality
Process 1 Process 2 Process 3
Store (flag1),1; Load r1, (flag1); Load r2, (flag2);
Store (flag2),1; Load r3, (flag1);
Question: Is it possible that r1=1 and r2=1 but r3=0 ?
  Sequential consistency: No

## Slide 17: Relaxed Consistency Models
Processor Consistency (PC)
  Intel / AMD x86, SPARC (they have some differences)
  Relax W→R ordering, but maintain W → W, R → W, and R → R orderings
  Allows in-order write buffers
  Does not confuse programmers too much
Weak Ordering (WO)
  Alpha, Itanium, ARM, PowerPC (they have some differences)
  Relax all orderings
  Use memory fence instruction when ordering is necessary
  Use synchronization library, don’t write your own
      acquire
      fence
      critical section
      fence
      release

## Slide 18: Weaker Memory Models
Architectures with weaker memory models provide memory fence instructions to prevent otherwise permitted reorderings of loads and stores
Fencewr
Store (a1), r2;
Load r1, (a2);
Fencerr;
Fencerw;
Fenceww;
The Load and Store can be reordered if a1 =/= a2.
Insertion of Fencewr will disallow this reordering
Similarly:
SUN’s Sparc: MEMBAR;
MEMBARRR; MEMBARRW; MEMBARWR; MEMBARWW
PowerPC: Sync; EIEIO
Slides from Prof. Arvind, MIT

## Slide 19: Enforcing Ordering using Fences
  Processor 1 Processor 2
    Store (a),10; L: Load r1, (flag);
    Store (flag),1; if r1 == 0 goto L;
    Load r2, (a);
  Processor 1 Processor 2
    Store (a),10; L: Load r1, (flag);
    Fenceww; if r1 == 0 goto L;
    Store (flag),1; Fencerr; Load r2, (a);
Weak ordering
Slides from Prof. Arvind, MIT

## Slide 20: Backlash in the architecture community
Abandon weaker memory models in favor of SC by employing aggressive “speculative execution” tricks.
  all modern microprocessors have some ability to execute instructions speculatively, i.e., ability to kill instructions if something goes wrong (e.g. branch prediction)
  treat all loads and stores that are executed out of order as speculative and kill them if we determine that SC is about to be violated.
Slides from Prof. Arvind, MIT

## Slide 21: Aggressive SC Implementations
Loads can complete speculatively and out of order
  Processor 1 Processor 2
  Load r1, (flag); Store (a),10;
  Load r2, (a);
miss
hit
Complex implementations, and still not as efficient as weaker memory model
kill Load(a) and the subsequent instructions if Store(a) commits before Load(flag) commits
How to implement the checks?
  Re-execute speculative load at commit to see if value changes
  Search speculative load queue for each incoming cache invalidate
Slides from Prof. Arvind, MIT

## Slide 22: Properly Synchronized Programs
Very few programmers do programming that relies on SC; instead higher-level synchronization primitives are used
  locks, semaphores, monitors, atomic transactions
A “properly synchronized program” is one where each shared writable variable is protected (say, by a lock) so that there is no race in updating the variable.
  There is still race to get the lock
  There is no way to check if a program is properly synchronized
For properly synchronized programs, instruction reordering does not matter as long as updated values are committed before leaving a locked region.
Slides from Prof. Arvind, MIT

## Slide 23: Release Consistency
Only care about inter-processor memory ordering at thread synchronization points, not in between
Can treat all synchronization instructions as the only ordering points
  …
  Acquire(lock) // All following loads get most recent written values
  … Read and write shared data ..
  Release(lock) // All preceding writes are globally visible before
  // lock is freed.
  …
Slides from Prof. Arvind, MIT

## Slide 24: Programming Language Memory Models
We have focused on ISA level memory model and consistency issues
But most programmers never write at assembly level and rely on language-level memory model
An open research problem is how to specify and implement a sensible memory model at the language level. Difficulties:
  Programmer wishes to be unaware of detailed memory layout of data structures
  Compiler wishes to reorder primitive memory operations to improve performance
  Programmer would prefer not to have to develop dead-lock free locking protocols
Slides from Prof. Arvind, MIT

## Slide 25: Takeaway
High-level parallel programming should be oblivious of memory model issues.
  Programmer should not be affected by changes in the memory model
SC is too low level for a programming model. High-level programming should be based on critical sections & locks, atomic transactions, monitors, ...
ISA definition for Load, Store, Memory Fence, synchronization instructions should
  Be precise
  Permit maximum flexibility in hardware implementation
  Permit efficient implementation of high-level parallel constructs.
Slides from Prof. Arvind, MIT