## Slide 1: Lock Basics
Jaehyuk Huh
Computer Science, KAIST

## Slide 2: Consistency Model

## Slide 3: Lock in Shared Memory
Spin locks: processor continuously tries to acquire, spinning around a loop trying to get the lock
Lock acquire
li R2,#1 lockit: lw R3,0(R1) ;load var bnez R3,lockit ;≠ 0  not free  spin
sw R2,0(R1)
  Does it work?
Lock release
sw R0,0(R1) ; R0 = 0

## Slide 4: Why Need Atomic Load and Store
thread 0 thread 1
li R2,#1 li R2,#1
lw R3,0(R1) lw R3,0(R1)
bnez R3,lockit bnez R3,lockit
sw R2,0(R1)
sw R2,0(R1)
Both threads can acquire the lock  why?
Value should not change between load and store  need atomic load and store

## Slide 5: Hardware Support For Locks
Atomic exchange: interchange a value in a register for a value in memory
  0  synchronization variable is free
  1  synchronization variable is locked and unavailable
  Set register to 1 & swap
  New value in register determines success in getting lock 0 if you succeeded in setting the lock (you were first) 1 if other processor had already claimed access
  Key is that exchange operation is indivisible
Test-and-set: tests a value and sets it if the value passes the test
Fetch-and-increment: it returns the value of a memory location and atomically increments it
  0  synchronization variable is free

## Slide 6: Spin Lock Implementation
Spin locks with atomic exchange
li R2,#1 lockit: exch R2,0(R1) ;atomic exchange bnez R2,lockit ;already locked?
What about MP with cache coherency?
  Want to spin on cache copy to avoid full memory latency
  Likely to get cache hits for such variables

## Slide 7: Spin Lock Implementation
Problem: exchange includes a write, which invalidates all other copies; this generates considerable bus traffic
Solution: start by simply repeatedly reading the variable; when it changes, then try exchange (“test and test&set”):
try: li R2,#1 lockit: lw R3,0(R1) ;load var bnez R3,lockit ;≠ 0  not free  spin exch R2,0(R1) ;atomic exchange bnez R2,try ;already locked?

## Slide 8: Hardware Support For Locks
Hard to have read & write in 1 instruction: use 2 instead
Load linked (or load locked) + store conditional
  Load linked returns the initial value
  Store conditional returns 1 if it succeeds (no other store to same memory location since preceding load) and 0 otherwise
Example doing atomic swap with LL & SC:
try: mov R3,R4 ; mov exchange value ll R2,0(R1) ; load linked sc R3,0(R1) ; store conditional beqz R3,try ; branch store fails (R3 = 0) mov R4,R2 ; put load value in R4
Example doing fetch & increment with LL & SC:
try: ll R2,0(R1) ; load linked addi R2,R2,#1 ; increment (OK if reg–reg) sc R2,0(R1) ; store conditional beqz R2,try ; branch store fails (R2 = 0)

## Slide 9: Lock Implementation : LL & SC
Using LL & SC to implement lock
LL does not cause any bus traffic
lockit: ll R2,0(R1) ;load var bnez R2,lockit ;≠ 0  not free  spin
daddui R2,R0,#1
sc R2,0(R1) bnez R2,lockit

## Slide 10: How to Implement Atomic Load-Store
Atomic exchange (or atomic load-and-store)
  Separate load and store internally by HW (one instruction visible to SW)
  Load part invalidate other caches
  Until store part is completed, any invalidation from other cache is held (if other processors need to write to the variable, make them wait)
Load-locked / store-conditional
  Remember the last load-locked address
  Invalidation from other processors set load-locked address to 0
  Store-conditional fail if load-locked address is 0

## Slide 11: Programming With Locks
Writing good programs with locks is tricky
Coarse-grained lock
  One lock for large data structure shared by many processors
  The entire data structure may not be used by all processors
  Programming is simple, but performance will be bad (too much lock contention)
Fine-grained lock
  Many fine-grained locks for different parts of large data structure
  Different parts may be updated by multiple processors simultaneously
  Programming is difficult to maintain many locks
Can HW remove the need for locks?

## Slide 12: Programming with Locks
Avoid data race condition in parallel programs
  Multiple threads access a shared memory location with an undetermined accessing order and at least one access is write
  Example: what if every thread executes total_count += local_count, when total_count is a global variable? (without proper synchronization)
Writing highly parallel and correctly synchronized programs is difficult
  Correct parallel program: no data race  shared data must be protected by locks
Common problems with locking
  Priority inversion: higher-priority process waits for a lower-priority process holding a lock
  Lock convoying: occur with high contention on locks
  Deadlock problem: get worse with many fine-grained locks
Locking granularity issues

## Slide 13: Coarse-Grain Locks
Lock the entire data structure  correct but slow
+ Easy to guarantee the correctness: avoid any possible interference by multiple threads
- Limit parallelism: only a single thread is allowed to access the data at a time
Example
  struct acct_t accounts [MAX_ACCT]
  acquire (lock);
  if (accounts[id].balance >= amount) {
  accounts[id].balance -= amount;
  give_cash();
  }
  release (lock)

## Slide 14: Fine-Grain Locks
Lock part of shared data structure  more parallel but difficult to program
+ Reduce locked portion by a processor at a time  fast
- Difficult to make correct  easy to make mistakes
- May require multiple locks for a task  deadlocks
Example
  struct acct_t accounts [MAX_ACCT]
  acquire (accounts[id].lock);
  if (accounts[id].balance >= amount) {
  accounts[id].balance -= amount;
  give_cash();
  }
  release (accounts[id].lock)

## Slide 15: Difficulty of Fine-grain Locks
May need multiple locks for a task
  Example: account-to-account transfer  need two locks
  acquire (accounts[id_from].lock);
  acquire (accounts[id_to].lock);
  if (accounts[id_from].balance >= amount) {
  accounts[id_from].balance -= amount;
  accounts[id_to].balance += amount;
  }
  release (accounts[id_from].lock)
  release (accounts[id_to].lock)
Deadlock : circular wait for shared resources
  Thread 0 : id_from = 10, id_to = 20
  Thread 1 : id_from = 20, id_to = 10
  Thread 0 Thread 1
  acquire (accounts[10].lock) acquire (accounts[20].lock)
  // try acquire (accounts[20].lock // try acquire (accounts[10].lock)
  // waiting for accounts[20].lock // waiting for accounts[10.lock

## Slide 16: Difficulty of Fine-grain Locks II
Avoiding deadlock: acquire all locks in the same order
Many more complex cases with locks
  Lock-based programming is difficult  easy to make mistakes
  May lead to deadlocks or performance issues
  May cause race conditions, if locks are not programmed carefully
  id_first = min (id_from, id_to)
  id_second = max (id_from, id_to)
  acquire (accounts[id_first].lock);
  acquire (accounts[id_second].lock);
  if (accounts[id_from].balance >= amount) {
  accounts[id_from].balance -= amount;
  accounts[id_to].balance += amount;
  }
  release (accounts[id_second].lock)
  release (accounts[id_first].lock)

## Slide 17: Lock Overhead with No Contention
Lock variables do not contain real data  lock variables are used just to make program exuection correct
  Consume extra memory (and cache space)  worse with fine-grain locks
Acquiring locks is expensive
  Require the use of slow atomic instructions (atomic swap, load-linked/store-conditional)
  Require write permissions
Efficient parallel programs must not have a lot of lock contention
  Most of time, locks don’t do anything  one thread is accessing a shared location at a time
  Still locks need to be acquired to protect a shared location (for example, 1% of total accesses)